Bottle Stripper Technical Notes

# Theory of Operation
Equation for strip width: strip cut width = delta Z/rotation. So the G-code for strip width of 8 mm is
G1 Z8 Y-360. . Or strip width = dz/(dy degrees/360). Or dy given dz and width = dz/width*360
# Using Marlin firmware
Z axis is negative up. 2 mm per rotation screw.
Y axis rotates bottle. Set up so 1 unit of movement is 1 degree. Positive is CCW viewed from the top.
# Test Data

Going up, F600 stalls motor, F400 does not.
Going down, F100 is quiet, F200+ vibrates.
Going down, M201 Z200 sometimes stalls.
G1 F8000 Yx is not too fast, and as fast as we’d ever need to go.

# Changes
- Z steps/mm: M92 Z1600
- Z max acceleration: M201 Z100
- Z max feedrate: M203 Z400
- Y steps/degree: M92 Y177.5
- Y max acceleration: M201 Y200
- Y max feedrate: M203 Y2000
# Known Issues
- Motor stalls: too much acceleration and/or too low stall limits
- How to set bottom cut location?
- Mount sideways so bottom removed by gravity?
- Variable bottle diameters: use tension strap and roller bearings?
- Display not mounted.
- Cut rate not coordinated with putrusion rate
- M117 command not respected
- M25 no way to recover or being ignored
- Need reset button
- G1 Z F300 makes a noisy motor, but F400 doesn’t. F600 okay F650,700,800 noisy. F900 stalls.
- Neck broke after I cut a relief for tightening it
  - Increase upper diameter from 23 to 27.5.
  - Remove slop in keyway. Reduce slot width from 3.42 to 3.15.
  - Remove stress concentration by chamfering between upper and lower cylinders.
  - Cut relief slot
- Need easier way to remove bottle after interrupted cut. Strip is in the way of easy removal.
- Need crash detection for bottle bottoming out if not cut. Limit switch? Stall detection?
- Need recut option. Use filament change macro?
- Beveled blade causes friction after cut as top side of cut bottle is lower than cut edge. Need Blade angle to match/exceed bevel or non-beveled top edge.
  OR Hot wire cutter?
- Bottles not finishing. Motor skipping steps? 2X times left 50 mm uncut.
- Firmware M154 not supported.