## Slide 1
Marc Caina
Tyler Johns
Antonio Mendoza
Christian Ventouras
Nicholas Wedyck
Notes: Marc

## Slide 2: Outline
Background
  Green Ellipses
  Key Terms
  Reclamation Process
  Recreator Pultrusion
Problem Statement
Design Requirements
Design Constraints
Automation Candidates
Process Down Selection
Design Ideas
Notes: Marc

## Slide 3: Green Ellipsis Background
“Green Ellipsis Dreams of and Designs for a Sustainable Humanity”
3D-Printing - Open-source Pultrusion Community
Start-up company based out of St. Augustine
Focuses on Upcycling Two Liter PET Bottles into functioning filament
Notes: Marc

## Slide 4: Key Terms
Polyethylene Terephthalate (ter·eph·thal·ate) [PET] - Commonly used plastic
Upcycling – the process of repurposing single-use items, such as plastic bottles, to create a product of higher quality or value
Pultrusion – a process for manufacturing plastics via pulling
Notes: Marc

## Slide 5: PET Reclamation Process
Bottle Cleaning
Bottle Cutting
Filament Splicing
Filament Packaging
By-Product Processing
Strip Pultrusion
Filament Winding
Notes: Christian

## Slide 6: Green Ellipsis Recreator Pultruder
[1] Green Ellipsis YouTube
Notes: Christian

## Slide 7: Reclaimed PET
Must be extruded at 130% flow rate
Melt temp at 225-245 ℃
Bed temp 65-85 ℃
Nozzle 0.4mm
Print Speed 30-60 mm/s
[2] rPET
Notes: Christian

## Slide 8: Problem Statement
Single-use PET bottles causes an abundance of pollution
Aim to upcycle bottles and convert them into 3D filament
Automation of at least one step in the Reclamation Process is required
Reclamation Processes
Notes: Tony

## Slide 9: Design Requirements
Reduce duration of reclamation process by 20 percent
Reduce human interaction by 50 percent for the bottle cutting step
Bottle cutting process must accept washed two-liter PET bottles
Must begin the pultrusion strip by cutting a 1.75mm wide ribbon from the bottle
Notes: Tony

## Slide 10: Design Constraints
Machine needs to fit in a 75cm by 240cm by 80cm volume
Must run off standard wall power (120Vac/60hz)
User must not be able to cut themselves easily
Use two-liter Pepsi product PET bottles
$1,000 budget
Notes: Tony

## Slide 11: Automation Candidates
Bottle Cleaning
Bottle Cutting
Strip Pultrusion
Notes: Nick

## Slide 12: Process Down Selection
Analytical Hierarchy Process (AHP)
Normalized Weights
Five Point Scale
Notes: Nick

## Slide 13: Design Ideas – Bottle Cutting Idea 1
Similar to Current Design
Bottom Gets Cut
Blade Pivots
Strip Gets Started
Notes: Nick

## Slide 14: Design Ideas – Bottle Cutting Idea 2
Bottle Placed Horizontally and held by cap fixture
Bottle is rotated to make strips
Initial cut removes the bottom before blade starts moving
Blade moves as bottle rotates until a limit switch is triggered
Notes: Tyler

## Slide 15: Design Ideas – Bottle Cutting Idea 3
Fixture is separate from cleaning and pultrusion steps
Clamps latch on to bottom of bottle
Rollers spin bottle while blades cut bottom off and start strip cutting
Notes: Tyler

## Slide 16: Questions?
Notes: Tyler

## Slide 17: References
[1] B. Alano, “Tension rod-less Recreator3D with runout detection,” YouTube, 12-Jul-2022. [Online]. Available: https://www.youtube.com/watch?v=w-EAWBNNP8s&amp;feature=emb_logo. [Accessed: 06-Oct-2022].
[2] RPET, “Ultrafuse® RPET - BASF Forward AM,” BASF 3D Printing Materials and Services, 18-Aug-2022. [Online]. Available: https://forward-am.com/material-portfolio/ultrafuse-filaments-for-fused-filaments-fabrication-fff/standard-filaments/ultrafuse-rpet/. [Accessed: 06-Oct-2022].